## Slide 1: title
DEPARTMENT OF BIOMEDICAL ENGINEERING
POSTURE DETECTION WITH VIBROTACTILE FEEDBACK
UNDER THE GUIDANCE SUBMITTED BY
P . RAJALAKSHMI KAVIYA S - 113123UG01024
ASSISTANT PROFESSOR POOVIZHI K - 113123UG01041
KAVYA KAMATCHI V - 113123UG01025

## Slide 2: Aim
To design a wearable posture monitoring system
To detect spine bending using sensors
To provide real-time vibrotactile feedback
To help users maintain correct posture.

## Slide 3: Objective
To measure body tilt using MPU6050 sensor
To calculate spine bending angle
To set a threshold limit for posture
To alert user using vibration motor
To indicate posture status using LCD
To develop a low-cost embedded system

## Slide 4: Scope
Can be used by students and office workers
Helps prevent back pain and posture-related problems
Useful in physiotherapy and rehabilitation
Can be upgraded with mobile app integration
Can be used in smart wearable devices

## Slide 5: Literature Review
S. No | SOURCE | PURPOSE | RESULT
1 | Wearable Real-Time Intelligent Posture Corrective System Using Vibrotactile Feedback (2011) | Real-time posture monitoring and correction | Vibration alerts Improved posture through vibration alert
2 | Intelligent Vibrotactile Biofeedback System (2012) | Posture correction on un-stable surface | Better balance and posture control achieved
3 | Wearable Posture Monitoring System with Vibration Feedback (2018) | Continuous posture tracking | Real-time detection and correction possible

## Slide 6: Literature Review
S. No | SOURCE | PURPOSE | RESULT
4 | Reducing Postural Load in Order Picking Through a Smart Workwear System Using RealTime Vibrotactile Feedback (2020) | Improve worker posture during industrial tasks | Reduced adverse trunk and upper arm postures; users found the system comfortable and effective
5 | Real-Time Human Posture Recognition Using Inertial Sensors (2017) | Detect body orientation and posture changes | High recognition accuracy with low computational cost
6 | Posture Monitoring System Using MPU6050 and Arduino (2021) | Low-cost posture correction device | Accurate detection of forward bending posture

## Slide 7: Summary of Literature
Existing systems focus on monitoring posture
Many systems are expensive or complex
Real-time feedback is limited in some designs
Need for affordable and wearable solution
Proposed system provides simple and effective feedback

## Slide 8: Methodology
Methodology (Step 1) :
MPU6050 sensor placed on lower back
Sensor measures acceleration values
Data sent to Arduino using I2C communication
Arduino processes the sensor data

## Slide 9: Methodology
Methodology (Step 2) :
Angle calculated from sensor values
Compared with predefined threshold
If angle exceeds limit:
  Vibration motor activated
  Buzzer and LCD turns ON
If posture is correct:
  Motor OFF
  Buzzer and LCD OFF

## Slide 10: Novelty in Research Proposal
Introduces a real-time posture correction system using vibrotactile feedback
Combines MPU6050 sensor with a simple embedded controller for accurate angle detection
Provides instant vibration alert instead of only monitoring (active correction approach)
Designed as a low-cost and portable wearable device
Uses threshold-based intelligent feedback mechanism
Simple design compared to complex IoT or camera-based systems

## Slide 11: Block Diagram

## Slide 12: Block Diagram Explanation
Sensor detects body movement and tilt
Arduino receives and processes data
Angle is calculated using formula
Compared with threshold value
If posture is incorrect:
  Motor vibrates
  Buzzer gets ON and LCD display “Posture Incorrect”
Provides instant feedback to use

## Slide 13: Result
System detects posture accurately
Real-time monitoring achieved
Vibration feedback works properly
LCD indication is clear
System responds quickly
Observation:
➢Correct posture → No vibration
➢Incorrect posture → Immediate alert
➢Stable performance during testing
➢Works continuously without delay

## Slide 14: Discussion
System is simple and efficient
Low power consumption
Accuracy depends on sensor placement
Threshold value can be adjusted
Useful for daily posture correction

## Slide 15: Conclusion
Provides real-time vibrotactile feedback
Helps improve posture habits
Prevents long-term spinal issues
Cost-effective and user-friendly

## Slide 16: Future the Scope
Integration with mobile application
Use of AI for posture analysis
Wireless communication (Bluetooth)
Smaller and more compact design
Data storage and tracking system

## Slide 17: References
Gopalai, A. A., & Senanayake, S. M. N. A., "A Wearable Real-Time Intelligent Posture Corrective System Using Vibrotactile Feedback," IEEE/ASME Transactions on Mechatronics, 2011.
Zheng, Y., & Morrell, J., "A Vibrotactile Feedback Approach to Posture Guidance," IEEE Haptics Symposium, 2010.
Xu, J. et al., "Configurable Wearable Sensing and Vibrotactile Feedback System for Real-Time Postural Balance and Gait Training," JNER, 2017.
Lins, C. et al., "A Wearable Vibrotactile Interface for Unfavorable Posture Awareness Warning," ICT4AWE, 2018.
Ishac, K., & Suzuki, K., "LifeChair: A Conductive Fabric Sensor-Based Smart Cushion for Actively Shaping Sitting Posture," Sensors, 2018.
Kim, W. et al., "A Directional Vibrotactile Feedback Interface for Ergonomic Postural Adjustment," IEEE Transactions on Haptics, 2021.

## Slide 18
Thank you